## Slide 1
The Problem: Threading a Narrow Window
Task
• A dual-arm omnidirectional aerial robot carries a box from a desk, through a partially-open tilted awning window, to a shelf.
• Threading the gap needs whole-body reconfiguration while holding the box.
[ IsaacSim scene / overview image ]
Two baselines fall short
• Pure sampling (geometric): no dynamic feasibility, cannot encode smooth dynamics or quadratic costs (e.g. keep the box under the base to cut load torque).
• Pure optimization (naive seed): non-convex collision constraints trap it in infeasible local minima; it does not converge.
Init. strategy | Conv. | Time (s) | Result
Naive OCP | 0/10 | — | no solution
Linear-interp OCP | 0/10 | — | no solution
Sampling-seeded | ✓ | 479 | grazes (−2.7 cm)
Keyframe (ours) | ✓ | ~1700 | clear (+2.8 cm)
OMPL (geometric) | path | ~20 | kinematic only

## Slide 2
Our Idea: A Single Keyframe as the Seed
[ Video: Sampling-seeded (sideways yaw twist) ]
[ Video: Keyframe-guided (ours) (natural pitch-forward) ]
Sampling-seeded: a sampler path seeds the OCP — it passes but twists sideways and grazes the frame.
Keyframe-guided: one keyframe selects the passage — a natural pitch-forward motion with more clearance.
The OCP seed decides everything. We build it from a single keyframe: the drone pose at the window, set by a human in the simulator, interpolated on the grasp manifold into the seed and a soft waypoint guide.

## Slide 3
The Result: A Better, Safer Passage
Quality of the collision-free passages
Metric | Sampling | Keyframe (ours)
Min. clearance (cm) | −2.7 | +2.8
Penetrating knots | 2 / 149 | 0 / 149
Base rot. path (deg) | 327.8 | 251.2
Base transl. path (m) | 11.54 | 10.13
Robust to the keyframe pitch
Keyframe pitch | Conv. | Pitch-fwd | Clear (cm)
50° | ✓ | yes | +5.4
60° (ref) | ✓ | yes | +6.8
70° | ✓ | yes | +4.3
• T2: keyframe clears the frame with less wasted whole-body rotation.
• T3: a ±10° keyframe still reaches the same safe passage.
Conclusion: a single human keyframe steers the optimizer into a better, safer homotopy — a natural pitch-forward passage with more clearance.